## Slide 1: “Prediction of the Effect of Solvents and Impurities/Additives on Crystal Shape and Growth Kinetics” ADDICT Advanced Design and Development of Industrial Crystallization Technology
Michael Doherty
UCSB Chemical Engineering
10 January 2019
Additional notes by John Hone

## Slide 2: Abstract
“The goal of this research is to develop a practical engineering tool
for predicting the relative growth rates (growth kinetics) and
morphology of solution-grown faceted crystals, including the effects
of solvent (Phase 1 of the research), and impurities/ additives (Phase 2).”
Solvent model exists and validated → now needs incorporation into ADDICT code.
Supersaturation model exists, needs validation then incorporation into ADDICT code.
Impurity model exists (validated on 2 case studies)
  deficient at high density facet coverages and needs improvement for some lower coverage scenarios. In the IFPRI 2019 work plan.

## Slide 3: The Team
Mike Doherty, PI – manage and oversee project
Dr. Yongsheng Zhao, postdoc – solvent effects & ADDICT growth rate engine
Steven Landis, Computer Science undergraduate – in charge of software and chief software developer
Toby Mazal – newly recruited doctoral student – impurity effects
      (Toby was a top undergraduate in ChE from the University of Delaware. He joined
      UCSB in September, 2018 as a first year doctoral student and comes with a partial
      Fellowship that combined with IFPRI funds will provide him with a full doctoral stipend)

## Slide 4
ADDICT executes a multiscale mechanistic framework
Models at each scale feed info back and forth
Crystal Shape
Crystal Face
Spiral /
2D Nuclei
Crystal Step
Kink Site
Kink Attachment / Detachment event
~ mm3
~ mm2
~100s nm
~ μm2
~ nm
What faces?
What mechanisms?
What step edges?
What kink cycles?
What step surface structures?
Net incorporation
rates
Step velocities
Kink densities
Spiral rotation times
Face growth rates

## Slide 5
Growth conditions
- Solvent & Impurity
- Supersaturation
- Temperature
Crystallography +
Interpret crystal
Describe growth units
Energetic calculations
Organize interactions
Mechanistic models
Spiral growth
ADDICT is a shape prediction tool
Computational screening can target experiments
ADDICT
Question:
How can we engineer the morphology by changing growth conditions?
ADDICT:
Fast computational screening + mechanistic insight into modifications can aid selection of growth conditions
Outputs
Inputs
Crystal shape
Lattice energy
Spiral & 2D nucleation and growth shapes
Mechanistic info (faces, steps, kinks etc.)
Morphology map

## Slide 6
Then use solvent sweep to shortlist solvents
Investigate shortlisted solvents experimentally
Crystallography
Specific polymorph
Pure organic molecule
Future: cocrystals/ solvates, organic salts
Growth conditions
47 solvents
Supersaturation
Temperature
Output = predicted morphology
Morphology map plots results of solvent sweep
Plot of 2nd vs. 3rd slowest growing face families relative to the slowest growing face family

## Slide 7: Shape Triangle
Organizes crystals by shape
Each circle is a crystal
Each vertex of the triangle is some ideal shape (Needle, Plate, Cube)
Quickly find growth conditions for specific shapes
Predicted morphology placed in a bounding cuboid; l, w, h analysed

## Slide 8: Next Steps For 2019
Test ADDICT for complex crystalline solutes (Z’ = 2 or greater)
Test for supersaturation-dependent shapes
Develop morphology models that incorporate impurity effects
Sensitivity analysis
Create detailed output and log files (shapes of spirals & 2D nuclei, …)

## Slide 9: JH Notes
Effect | Initial Model | Final Model | Validation | Coded in ADDICT
Temperature | ü | ü | ü | ü
Solvent | ü | ü | ü | 2019
Supersaturation | ü | ü | 2019 | 2019
Impurities (IFPRI) | ü | 2019 | 2020 | 2020