## Slide 1
Stefan Bellinghausen – PSE
19th April 2021
Methods and Specifications for Particle Properties
IFPRI roundtable

## Slide 2: Design considerations from modelling perspective
QbD: Importance of process understanding
  Basis for process modelling/experimental design
    Quality instead of quantity
    Identify critical experimental conditions
  Monitor all key (input/output) properties – e.g. full PSD, particle porosity
Predictive modelling
  Only estimate most impactful parameters
  Avoid re-estimation of parameters (per experiment/scale/etc)
  -> Reduce experimental effort
  -> Improve model predictions
Chart: Input
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 | Category 6 | Category 7 | Category 8
Series 1 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3
Statistical
Recom-mended focus

## Slide 3: Model-driven workflow
Model validation & uncertainty analysis
Process data
Parameter estimation(s)
Experiment design for parameter accuracy
Experiment design for model discrimination
Experimental data sets
Import data
Experimental set-up
Experimental data for fitting
Experimental data for validation
Fitted parameters
Validated model

Not validated to sufficient accuracy
Model equipment & sensors
Model candidates for e.g. reaction kinetic mechanisms
Model of experimental setup
Model validation cycle
Success
Import data
Validated model
Model equipment & sensors
Notes: …this requires an understanding of how to validate the models. This slide shows the workflow required to achieve this. Firstly we start with a model and perform some experiments to generate some targeted data. The data is split, using some cross-validation techniques, to estimate the parameters and blind test or externally validate the model. The results of this model validation can then be assessed to determine the predictive quality of the model. A key point at this stage is to quantify the model uncertainty and determine if it is within reasonable bounds.