## Slide 1: Bruno’s personal experience in big pharma (1 of 3)

## Slide 2: Bruno’s personal experience in big pharma (1 of 3)
Most of the time the focus is on particle size (rather that surface area, particle shape, etc) because it is “easier to measure”
  This is an assumption that isn’t always true
At product launch we typically have experience making less than 20 lots of a new active ingredient
Regulatory agencies (like the FDA) want to use that very limited experience to define the particle property release specifications for the lifetime of the product (could be the next 20+ years)
Approaches other than using this so-called “lot history” struggle to gain acceptance

## Slide 3: Hypothetical example: Lot history approach
Lot # | D10 (um) | D50 (um) | D90 (um) | Lot size/use
#AS1289G | 12 | 19 | 33 | Small scale, lab trials
#12555FFBJ | 21 | 23 | 35 | Small scale, clinical
#0098IK78 | 22 | 28 | 41 | Pilot scale, site A
#POL3893y298 | 35 | 42 | 55 | Pilot scale, site A
#A2345 | 15 | 20 | 32 | Pilot scale, site B
#GG89720 | 11 | 20 | 35 | Pilot scale, site B
#1111908 | 13 | 21 | 33 | Commercial site
#08908HJL | 20 | 24 | 36 | Commercial site
Range (n=8) | 11 - 35 | 19 - 42 | 32 – 55 | 
What commercial specifications would you propose based on this data set?

## Slide 4: Bruno’s personal experience in big pharma (2 of 3)
Typically, we aim for a two-point particle size specifications
  Usually this includes a center point (such as D(50)) and an upper particle size limit (such as D(90))
  Together these parameters also describe the spread of the particle size distribution
In the past few years there has been a strong push from regulatory agencies to:
  Set three-point specifications (such as D(10, D(50) and D(90))
  Set both upper and lower bounds for these parameters
This is driven by a sentiment that tighter specifications equate to lower lot-to-lot variability and this is always better

## Slide 5: Bruno’s personal experience in big pharma (2 of 3)
Where possible, we try to:
  Leverage mathematical models to support our proposed specifications
    For example, drug absorption models or tablet content uniformity models
    Try not to solely rely on lot-history
  Take into account method, instrument and operator variability
    Based on the results of gage R&R studies
  Use statistical approaches to predict future performance
    For example, use lot-history data to calculate 99% confidence limits for future lots
  Push for the widest possible limits to maximize future manufacturing flexibility